## Slide 1: UCNt Overview
UCN trap with very low intrinsic losses
  Magneto-gravitational trap
  Superposed holding field to eliminate B-field zeros (no depolarization losses)
  Fast removal of quasi-bound UCNs possible through trap asymmetry and field ripple
High statistics are achievable
  Large volume
  In situ UCN detector
    High overall efficiency
    Also: Less sensitive to phase-space evolution than draining
Based on original concept: P.L. Walstrom, J.D. Bowman, S.I. Penttila, C. Morris, A. Saunders, NIMA 599 (2009) 82-92
Notes: Scale of apparatus: ~2 m.
No material interactions.
No field zeros where Majorana spin flips could otherwise occur.
Mechanism to remove quasi-bound UCNs that would otherwise slowly leak out.
Large volume so statistics are achievable in a reasonable time.
Original concept was to detect betas that are guided by the holding field to detectors at the ends. Tests indicate the background is probably too high for this to be feasible. A new idea (besides the standard method of draining UCN into an external counter) is an “in situ” detector.
Details of prototype construction in next talk.
The prototype will serve as a test bed of the trap concept, detection schemes, and systematic effects.

## Slide 2: Halbach Array + Holding Field
(if continuous rotation of M)
η
ζ
d
w
Parameters:
d = 2.54 cm, w = 1.27 cm, Brem = 1.3 T
min. trapping field 0.82 T at 2 mm,
corresponds to mgh = |mnB| with
h = 0.48 m
Holding field eliminates field zeros
Notes: Exponential fall off of |B| from trap surface: Large effective volume for low-field seeking UCN. External electromagnetic coils provide a holding field everywhere normal to the Halbach array field: no field zeros. Walstrom et al. calculated completely negligible depolarization losses. Recent analysis by Steyrl which accounted for transverse velocities found much higher depolarization loss, but still negligible for a 0.1-s measurement.

## Slide 3: The UCNt experiment trap is formed by an array of ~5000 permanent magnets forming a “bathtub”

## Slide 4: Asymmetric Trap induces Phase Space Mixing
Adjacent Magnetization
out of phase
Higher
Curvature
PMs in a given row share same M alignment
Low symmetry, together with field ripples, enhance states mixing between (quasi)-periodic orbits through chaotic motion.
 quick cleaning (~ 10s of seconds) of the ‘quasi-bound’ UCN with large tangential velocities.
Two torus patches of different curvatures join along middle row
Notes: In fact, the main feature, other than the Halbach array, is the asymmetric geometry of the trap.
This asymmetry enhances mixing between periodic orbit, to accelerate the draining of the over-the-threshold, quasi-bound neutrons.
Magnets are lined on inner surfaces of two toroidal patches (with different radius of curvatures) pieced together along the middle row.
We only built the trap to 0.5 m high (due to budget constraint).
UCN trapping potential  50 neV
H=0.5 m in Earth gravity.
A matching B=0.8 T. (2 mm away from the array surface)

## Slide 5: UCNt Testbed: Magneto-gravitational storage vessel
UCNs
Halbach array of permanent magnets
No material interactions during storage period
In situ (V-foil activation) or ex situ (fill and dump) neutron detection possible
In situ detector
Halbach array
Cleaner
Ex situ monitor (10B)
Polarizer
Spin flipper
Al shutter

## Slide 6
UCN SD2 Source
Spallation driven by LANSCE 800 MeV proton accelerator
1m
Radiation Shielding
6T Pre-Polarizer Magnet (PPM)
Zr Vacuum Separation Foil
7T Polarizer Field
UCNA Spectrometer (1 UCN/c.c.)
UCNt Magneto-Gravitational Trap
Gate Valve (80 UCN/c.c.)
The UCN Experiment at LANSCE
UCNt
10B UCN Detector
Gate Valve
3He UCN Detector
Notes: The UCNtau experiment shared the UCN beam with the UCNA/B experiment.
Polarized UCN come down the guide after the pre-polarizing magnet. A spin-flipper was used to turn them into the low field seekers, that can be loaded inside the UCNtau trap.
We used various UCN flux monitor to measure the UCN flux, that will be used for N0 normalization.

## Slide 7: The UCNt experiment is installed in the UCN facility at Los Alamos’s LANSCE accelerator

## Slide 8: Removal of “Quasi-bound” UCNs
Quasi-bound (superbarrier) UCNs have energy above the trap potential but leak out slowly.
Trap asymmetry + field ripple from the array induces phase-space mixing.
An absorber placed near the top of the trap quickly removes the superbarrier UCNs.
Absorption time (s)
hclean = 44 cm
hclean = 42 cm
Simulation of trap cleaning
[Walstrom et al., NIMA 599 (2009) 82-92.]
Movable Absorber for trap “cleaning”
Notes: An absorber is lowered into the trap after filling, then retracted after some period << tau_n. Ideally the absorber covers the entire trap. In reality covering just part of the trap near one side may be good enough. (The trajectories shown are actually from Chen-Yu’s simulation.) [Key points: UCN are a non-interacting gas (non-ergotic); phase-space evolution; quasi-bound orbits and how that affects the measurement.]

## Slide 9: Measurement Cycle
Load the trap
Remove quasi-bound UCNs
Hold UCNs in the trap for time t
Count the surviving UCN population N
Using two different cycles with holding times t1 and t2,
Statistically most efficient if t2≈t1+2.2tn; then
UCN absorber
Al shutter
UCN monitor
UCN
Trap door
Notes: Explain “Holding time” vs. “Storage time”.
N1 and N2 must be normalized to the initially trapped population (post-cleaning), and detection efficiency must be the same for both cycles.

## Slide 10: “Fill and dump” measurement cycle: UCNs detected in ex situ monitor
1
2
3
4
5
0
0: Start UCN flow: beam on, shutter open, trap door open; cleaner inserted
1: Shutter closes
2: Filling and cleaning; superbarrier UCNs to monitor
3: Trap door closes, shutter opens; beam off; UCNs in guide to monitor; cleaning
4: Cleaner retracted; storage begins
5: Storage
6: Trap door opens; UCNs in trap to monitor
6

## Slide 11: First Storage Time Data (Feb. 2013)
t = 860 ± 19 s
(Draining method)
Salvat et al., PRC 89, 052501 (2014).

## Slide 12: Alternative to Draining: in situ Detection
Draining time could depend on holding time, causing systematic error.
In situ detection avoids transport losses to external detector.
A candidate in situ detector for UCNt is based on neutron absorption on vanadium.
Comparing lifetime measurements with the two methods could expose an otherwise elusive systematic effect.
NaI detector
Plastic scintillator
Store
Absorb
Count
V foil
UCN
Notes: Details in CY talk.

## Slide 13: The next step: in situ detection of surviving neutrons

## Slide 14
Cut Criteria:
beta event is not coincident with a beta event in the other detector
beta event pulse-height (460~8000).
beta event is coincident with an NaI event
NaI event a pulse-height (2500~3500)
anti-coincidence w/ other beta
a pulse-height cut on the beta spec.
Coincidence w/ NaI
Beam On
Beam Off
S/N= 2.28
=0.8
=0.3
S/N= 10
=0.8
=0.21
Notes: Currently, we are optimizing the detector performance to increases the S/N ratio, without sacrificing the signal rate.
With the V detector working, we can perform meaningful studies on the
time-dep. BG
N0 Normalization
The evolution of the UCN energy spectrum, by placing V at different height at the end of different storage time.

## Slide 15: The neutron absorber/detector in the lowered position

## Slide 16: The V absorber can rapidly count all the neutrons in the trap
Absorption time is at least an order of magnitude less than trap draining time
Can be reduced further by installing larger V foil, also testing systematic variations
Absorber can be positioned at different heights in the trap
Distribution of neutrons can be compared to MC models
Efficiency of cleaning can be tested by positioning foil above cleaning height

## Slide 17: Anticipated Statistical Reach
With present LANL source performance, we estimate up to ~105 UCN per fill (0.2 UCN/cc density).
Assume 50% detection efficiency: then ~50,000 detected UCN per fill.
Assume 3800 s per complete tn measurement (two complete cycles: one short, one long)
  Cycle time includes filling, cleaning, holding, and detection times.
Result: 44 hours live time required for dtn/tn ~ 0.1% (i.e., ~1 s statistical precision).
Enables precision studies of systematics.
Notes: If trap loading can be made very efficient. Need long guide lifetimes and low depolarization on the way into the trap. Projection based on experience acquired with UCNA. [Don’t read details; just conclusion. …this makes it possible to study systematics with precision.]

## Slide 18: Short-term UCNt R&D Goals
Statistics:
  Can we load enough UCNs into the trap?
  Can we detect surviving UCNs efficiently?
Systematics:
  Can we clean quasi-bound UCNs sufficiently?
  Can we accurately normalize the initial (cleaned) UCN population?
  Are there losses in the trap (e.g., heating or spin-flips)?
  Can we detect surviving UCNs without bias?
Our longer-term approach:
  Study the existing prototype apparatus to determine its ultimate reach.
  Explore possible upgrades to the existing prototype, or new ideas relevant for a next-generation experiment.
  Study systematic effects relevant for a next-generation experiment (e.g., by exaggerating an effect so it’s discernable at ~1-second precision).
  Develop high-fidelity UCN simulations to evaluate new designs.
Notes: Ultimate precision of prototype: probably at least ~1 second; what’s the limiting factor? Statistics? Some systematic effect that can’t be sufficiently characterized? Example possible upgrades to the prototype: active in-situ detector (to remove absorption-time and background issues); new ideas for UCN population normalization. Mention R&D proposal here?
Note from Mark on how to study heating: “The way heating has been studied in the past is by watching UCN boil out of an open topped vessel after it is cleaned down to some level. For the lifetime trap I proposed using an active cleaner as a detector. So first clean the trap to some depth. Then after varying amounts of time drop the cleaner back in and look for signals above the cleaned level. This could be done while manually adding vibrations to the system at different amplitudes and frequencies. You would also want to add electronic noise to the holding field and look for heating the same way.”

## Slide 19: Study Cleaning of Quasi-bound UCNs
Proof of principle detection of upscattering was done.
Things to be studied include:
  How to improve upscatter detection efficiency and background.
  Varying cleaner height and material
  Computer simulations of UCN trajectories in the trap
  Intentionally load a harder UCN spectrum; check for effect on storage time measurement.
3He detectors
Notes: Some 3He drift tubes were instrumented for first test run. We could e.g. look for any long-lifetime component in the observed upscattering time spectrum. Quasi-bound cleaning is a topic of Mark’s EC proposal.

## Slide 20
FY9 | FY10 | FY11 | FY12 | FY13 | FY14 | FY15 | FY16 | FY17 | FY18 | FY19 | FY20 | FY21
Simulations
Trap Design & Construction
Detectors
UCN Storage
UCN Transport
UCN Cleaning
UCN Heating
UCN Depol
DAQ
~ 1 sec t
Improved t
Simulations
Timeline
Notes: Simulations 1,2 5 13
Trap Design& Construction 2 4
UCN Transport 5 8
Detectors 5 8
UCN Storage6 8
UCN Cleaning 7 9
UCN Heating 7 9
UCN Depolarization7 9
DAQ 7 9
~1 sec Lifetime Measurement 8 10
Improved Lifetine 9 13

## Slide 21: Anticipated R&D Milestones
Milestone | Due Date
Demonstrate working vanadium detector and neutron transport simulations. | FY2015 Q1
Achieve sufficient UCN density in the trap for rapid 1 s measurements and an ultimate sub-1 s measurement. | FY2016 Q1
Complete DAQ for 1 s measurement; plan for control of all sub-1 s systematics. | FY2017 Q1
Publish 1 s measurement. | FY2017 Q3
Submit sub-1 s construction project proposal (if necessary). | FY2017 Q4
Notes: If no Mark EC award, the schedule will have to be delayed.

## Slide 22: High-level WBS for R&D Effort
Notes: The “Responsible Person/Institutes” may change for some tasks; we’re discussing this within the collaboration. Furthermore, we are actively recruiting new members to the collaboration [who have we approached?]; the R&D proposal document will serve as a convenient way to explain the R&D effort to a potential new collaborator.

## Slide 23: UCNt Collaboration
DePauw University
A. Komives
Hamilton College
G. Jones
Indiana University
E. R. Adamek, N. B. Callahan, W. Fox, C.-Y. Liu, D. J. Salvat, B. A. Slaughter, W. M. Snow, K. Solberg, J. Vanderwerp
JINR
E. I. Sharapov
LANL
D. Barlow, M. Blatnik, L. J. Broussard, S. M. Clayton, T. M. Ito, M. Makela, J. Medina, D. J. Morley, C. L. Morris, R. W. Pattie, J. Ramsey, A. Saunders, S. J. Seestrom, S. K. L. Sjue, P. Walstrom, Z. Wang, T. L. Womack
North Carolina State University
C. Cude-Woods, E. B. Dees, B. vornDick, A. R. Young, B. A. Zeck
ORNL
J. D. Bowman, S. I. Penttila
Tennessee Tech.
A. T. Holley
UCLA
K. P. Hickerson
Virginia Tech
X. Ding, B. Vogelaar
And special thanks to S. Clayton, C.-Y. Liu, and D. Salvat

## Slide 24: Extra Slides

## Slide 25: Possible budget scenarios
Chart: 
| 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022
DOE Operations | 250 | 250 | 250 | 250 | 250 | 250 | 250 | 250 | 250
LANL Internal | 1000 | 1000 | 1000 | 0 | 0 | 0
DOE R&D | 800 | 1000 | 1200 | 800 | 400 | 0
DOE Project | 600 | 1000 | 1600
Shifting from LANL Internal to DOE R&D to DOE Project
Development -> 1 s -> sub 1 s
DOE operations contributes to running UCN source

## Slide 26: Test setup (Feb. 2013)
UCN
Not shown: holding field coils
Al shutter

## Slide 27: Fill-and-Empty Measurement
UCN absorber
Al shutter
UCN monitor
UCN
Notes: Get rid of this sequence.

## Slide 28: Fill-and-Empty Measurement
UCN absorber
Al shutter
UCN monitor
UCN
Close shutter

## Slide 29: Fill-and-Empty Measurement
UCN absorber
Al shutter
UCN monitor
Close shutter
Beam off, close trap door, open shutter

## Slide 30: Fill-and-Empty Measurement
UCN absorber
Al shutter
UCN monitor
Close shutter
Beam off, close trap door, open shutter
Raise cleaner

## Slide 31: Fill-and-Empty Measurement
UCN absorber
Al shutter
UCN monitor
Close shutter
Beam off, close trap door, open shutter
Raise cleaner
Drain trap
Storage time
Notes: In this first UCNs data: loading efficiency is obviously not good. This is an R&D topic.

## Slide 32: Fill-and-Detect Measurement
UCN absorber
Al shutter
UCN monitor
Close shutter
Beam off, close trap door, open shutter
Raise cleaner
b and g detectors

## Slide 33: Fill-and-Detect Measurement
UCN absorber
Al shutter
UCN monitor
Close shutter
Beam off, close trap door, open shutter
Raise cleaner
Lower V foil, then raise V foil into det.
Storage time
b and g detectors

## Slide 34: Fill-and-Detect Measurement
UCN absorber
Al shutter
UCN monitor
Close shutter
Beam off, close trap door, open shutter
Raise cleaner
Lower V foil, then raise V foil into det.
Storage time
b and g detectors

## Slide 35: Fill-and-Detect Measurement
UCN absorber
Al shutter
UCN monitor
Close shutter
Beam off, close trap door, open shutter
Raise cleaner
Lower V foil, then raise V foil into det.
Storage time
b and g detectors
Time
52V Decays (simulated)
Notes: Replace 52V decay plot with simulated data, rather than show the data w/out the coincidence cut; we can fit exponential decay to get the initial number of parents and thus the number of absorbed UCNs.

## Slide 36: R&D for Trap Population Normalization
1000 second bins, linear drift
Test of UCN beam spectral stability:
Stability on the 0.1% level appears straightforward, but
How well does this test relate to the trapped population?
Further tests:
Implement a higher-resolution spectrum monitor
Test correlation of external monitors with post-cleaning trapped population (e.g., do many measurement cycles with the same holding time).
Use vanadium detector positioned at the top of the trap to count superbarrier UCNs; check if this can be a reliable normalization method.
From source
Notes: Test was effectively a very low resolution (3-level) spectrometer. Not sensitive to e.g. changes in polarization fraction or anything else that might affect the trap loading efficiency. Topic of Mark’s EC proposal.

## Slide 37: Study UCN Depolarization in the Trap
Can be data-driven:
  Compare 1-s lifetime measurements with
    holding field reduced;
    different trap surface coatings (copper vs. a UCN absorber?);
Active trap surface to directly detect high-field seekers?
Map the B-field inside the trap; run computer simulations of UCNs in the measured field (requires high-fidelity simulations).
Notes: Topic of Mark’s EC proposal.

## Slide 38: Develop High-Fidelity UCN Simulations
Two types of simulations
  Transport: track UCNs from the source to see how many trappable UCNs (low-field-seeking, sub-barrier) make it into the trap.
  Motion in Trap: track UCNs (position, polarization) within the trap for long periods (>2.2tn).
    Study phase-space evolution, Cleaning, Depolarization, Detection.
    High statistics may be required for subtle effects.
Strategy: develop high-fidelity simulations and validate them with measurements (e.g., with experimental parameters that enhance a systematic effect).
Long-term Goal: develop a predictive capability to reliably evaluate new designs before construction.
Notes: Led by Indiana University contingent. Re long-term goal: “new designs” could be for a novel detector, a new cross assembly, different trap geometry, different holding field, etc.

## Slide 39: R&D Scenarios for a Sub-1 s Experiment
We find systematic errors in the existing prototype can controlled to a level <0.01%, and loading efficiency is adequate.
  Proceed with sub-1 s measurement.
Same as 1, but we find the loading efficiency can not be improved enough for the desired statistical precision.
  Look for much more intense UCN source (if any successfully come online…)?
Same as 1, except we find some limiting systematic with the in situ vanadium detector technique (e.g., too sensitive to background drifts).
  Devise alternative in situ detector.
We find the UCNt method is sound, but major modification to the existing apparatus (or an entirely new apparatus) is required.
  Design an improved UCNt apparatus.
We find some fundamental problem with the UCNt concept.
  Study alternative experimental concepts; use computer simulations to evaluate them.
Notes: Delete. Scott will cover this.

## Slide 40: Neutron Trap Experiments
+ + +
Measures the Storage Time
Mambo (Mampe’s bottle)
Fomblin Oil
Vary V/A ratio
Mambo II: prespectrum
Notes: There are two ways to measure the neutron lifetime, however the averaged results from the two methods don’t agree with each other. The difference is larger than the error bars quoted by each class of experiment.
In this talk, I will focus on the means to trap low-energy neutrons, and measure its exponential decay time constant to infer the beta-decay lifetime.
The trouble is the neutron lifetime is just long enough, which is 15 mins, that its environment also impact strongly in how long they can live.
Neutrons can be absorbed by other nuclide, scattered and heated to gain enough energy to escape the trap, and there are also the subtle effect of the slow escape of quasi-bound neutrons that obscure extraction of the true beta-decay lifetime.

## Slide 41
Source location | Source type | UCN density [cm-3] | comment | when?
ILL Grenoble, PF2 | LD2 + turbine | 50 | still THE source | > 1985
Los Alamos, 2.4 kWav proton | SD2 | 120 | in source | now
Mainz TRIGA upgraded | SD2 | 20  200 | in V = 10 l | now 2009
ILL Grenoble, H172 upgraded + magnetic trap | He-II (0.5 K) | > 1000 2000 polarised | in V = 6.4 l up to 40 l | 2009 > 2011
PSI, 12 kWav proton | SD2 | > 1000 | in V = 2000 l | 2010
North Carolina, 1 MW reactor | SD2 | 1300 | in source | 2011
Munich, 20 MW reactor | SD2 |  10000 | in source | 2011
PNPI, 16 MW reactor | He-II (1.2 K) | 13000 7700 | in 35 l exp. bottle in 350 l exp. bottle | 2012
TRIUMF, 5 kWav proton | He-II (0.8 K) | 18000 | at exp. port | proposal
+ insitu He-II UCN sources at ILL (Cryo-EDM), NIST (n-lifetime), and SNS (EDM)
International competition in UCN production
Courtesy: O. Zimmer

## Slide 42: C. Y. Liu: UCNt Systematics

## Slide 43: Systematic Effects in the next Bottle Experiment
Chen-Yu Liu
Neutron Lifetime Workshop
Amherst
9/19/2014

## Slide 44: Bottle Technique
Survived UCN:
Measured by a UCN detector.
Equilibrium # of UCN in the trap:
inferred by a beam monitor (BM).
ep: polarization efficiency
eg: geometrical efficiency
ee: energy efficiency
Unpolarized
All E
Response time ~ 10m/(5m/s)~ 2 s
polarized
E < Ec
Response time ~ fill time~ 200 s
Lifetime extracted from the two-point measurement:

## Slide 45: “Fill and dump” measurement cycle: UCNs detected in ex situ monitor
1
2
3
4
5
0
6

## Slide 46: Normalization
Does the BM measure the right thing?
For constant flux (t) = 0
: equilibrium number of UCN in the trap
Fill time constant:
a geometrical factor:
Not exactly ¼.

## Slide 47: A Proper Normalization Scheme
A simulation result:
(t) right before the trapdoor closes weigh more heavily to the trapped population.

## Slide 48: Monte-Carlo Simulations
Another geometry with more quasi-bound neutrons:

## Slide 49: Quasi-bound Neutrons
If the QB neutrons are not sufficiently cleaned, they will leak out of the trap with its own characteristic time constant qb. The resulting correction time is:
Chart: 
| 10 | 20 | 30 | 40 | 50 | 100 | 200 | 765 | 781 | 881 | 1000 | 1800 | 2000 | 5000 | 10000 | 20000 | 100000 | 1000000
delta t | 8.9774e-09 | 0.00019774 | 0.005543 | 0.029346 | 0.07976 | 0.58866 | 1.5963 | 3.0115 | 3.0118 | 2.9972 | 2.9524 | 2.4418 | 2.3177 | 1.253 | 0.6964 | 0.36748 | 0.07677 | 0.0077531
t2 = 2000 s
t1 = 200 s
 = 0.01
t = 0.1 s
To limit t < 0.1 s for all qb ,
need  < 3e-4

## Slide 50
For UCN, the Halbach trap serves as a perfect mirror-like reflecting surface.
 Typical intuition with gas diffusion does not work.

## Slide 51: Easy in, easy out
Qausi-periodic trajectories

## Slide 52: UCN density vs. Height
0
For mono-energetic UCN:

## Slide 53: UCN Spectrum (C. Morris)
Chart: Velocity (cm/sec)
v3dv distribution, due to absorption and
other losses in a thick D2 source.
Chart: Height (cm)
Raise the experiment by 1 m
SS guide: 190 neV

## Slide 54: UCN Density inside the Trap
Factor to 3.3
A major UCNtau goal in 2014:
- Up the UCN statistics
  100,000 trapped inside the trap.
  1 UCN/c.c. at the trap door opening,  0.3 UCN/c.c averaged inside the trap.

## Slide 55: Sensitivity Optimization (with a constant BG)
Background subtracted signal
x = t/ = (t2-t1)/
S/N = 1
No BG
Constant background:
B1= B2 =  N0

## Slide 57: How well to measure each non-beta-decay loss?
need to measure τabs at the 10% level of precision.
+ + +
Each loss is a new degree of freedom, so this is a vector sum.
To achieve a correction time of 1 s:
12 days!
Set to be 1/10 of the desired uncertainty.
Notes: If the correction delta t = 100 sec, needs to measure at 1e-3 level.

## Slide 58: Polyatomic Gas cross sections
Include first order error from fitting.
Seestrom et al. (2014) to be submitted.

## Slide 59: Halbach Array Trap +  (copper tape)
 = (42.2  0.5) /33,632 = 0.1%
Cu loss per bounce: 1.55e-4
Notes: We have plans to patch up the missing magnet corners by grinding up our spare magnets to the exact shape.
For now, they are covered by copper tapes (with a total surface area about 40 cm^2, that 0.1% of the total surface area, with loss per bounce probability of 1e-4).
However, we estimate that the presence of these copper tapes can introduce a correction of lifetime to 0.5 sec.

## Slide 60: Material Loss
200s storage
Average collision time: 0.51 s
Chart: Time between collisions (s)
| 0.1 | 0.15 | 0.2 | 0.25 | 0.3 | 0.35 | 0.4 | 0.45 | 0.5 | 0.55000000000000004 | 0.6 | 0.65
 | 1.5069 | 1.0052 | 0.75411 | 0.60339 | 0.50289 | 0.43108 | 0.37722 | 0.33532 | 0.3018 | 0.27437 | 0.25151 | 0.23217
The time it takes a UCN to find Cu surface ~ 500 s, the time it takes to be absorbed by Cu ~ 105 to 106 s.
Spectrum averaged correction time:
t = 0.3 s

## Slide 61: Fermi potential vs thin-film oxide layer
Calculated without loss
in the film

## Slide 62: Systematic Effects
N0 normalization
  Source: intensity fluctuation, spectral change.
  N0 detector: efficiency change
  Polarization fluctuation
  Cleaner: height, timing fluctuation
  Insufficient filltime
Losses inside the trap
  Residual gas upscattering /absorption
  Depolarization: gradient depolarization, field-zero crossing, AFP spin flip
  UCN heating (mechanical vibrations)
  UCN heating (RF noise in the B0 field)
  Field holes (trap defect)
  Material interaction inside the trap.
  Leak through trapdoor
Phase space evolution
  Quasi-bound (marginally trapped) UCN: measure  vs cleaner height

## Slide 63
Work in progress !!!

## Slide 64: Backup Slides

## Slide 65: Poincare’s Section of Surface
Two degrees of freedom
Notes: In fact, the neutron trajectories are far more complex and interesting.
We use Poincare maps to study the UCN dynamics, by plotting the transverse velocity and radial velocity every time the neutrons collides the trap wall.
For a neutron with a fixed incoming energy, a series of curves plotted here representing varying incident polar angle. The azimuthal angle is fixed at 90 degrees, i.e., UCNs are coming in along the narrow side of the toroid.
The history of neutron on the Poincare map is confined by the continuous curve, and we call these quasi-periodic orbits.
If the neutron energy increases, these curves distort, and develop regions of stochastic behavior.
Chaos starts when the UCN reaches the focal point (~ R/2) of a circular concave mirror.
In fact, it is a symmetric bowl with (R_minor=0.5 m, R_major=1.0m). It is shown that Chaos exists even in a symmetric trap.

## Slide 66: Adiabatic Fast Passage (AFP) Spin Flipper Coils
Low field spin flipper
(low-pass bird cage resonator)
B0: 140 gauss
Resonant frequency: 400 kHz
Power: 1W

## Slide 67: Adiabatic Fast Passage Spin Flip Coils
Chart: AFP Field Map (Measurement, 5Amp)
Low field AFP spin flipper
B0 = 140 Gauss
RF frequency = 400 kHz
RF power = 4 W
B1 = 1.7 gauss

## Slide 68: RF power fluctuation
Chart: Spin flip efficiency
| 1 | 1.1000000000000001 | 1.2 | 1.3 | 1.4 | 1.5 | 1.6 | 1.7 | 1.8 | 1.9 | 2 | 2.1 | 2.2000000000000002 | 2.2999999999999998 | 2.4 | 2.5 | 2.6 | 2.7 | 2.8 | 2.9 | 3
epsilon | 0.99045 | 0.9921 | 0.99337 | 0.99435 | 0.99513 | 0.99575 | 0.99627 | 0.99669 | 0.99705 | 0.99735 | 0.99761 | 0.99783 | 0.99803 | 0.99819 | 0.99834 | 0.99847 | 0.99859 | 0.99869 | 0.99878 | 0.99886 | 0.99894
Chart: 
| 0.34602076124567477 | 0.41868512110726647 | 0.49826989619377171 | 0.58477508650519039 | 0.67820069204152245 | 0.7785467128027681 | 0.88581314878892747 | 1 | 1.1211072664359862 | 1.2491349480968859 | 1.3840830449826991 | 1.5259515570934257 | 1.6747404844290659 | 1.830449826989619 | 1.9930795847750868 | 2.1626297577854676 | 2.3391003460207616 | 2.5224913494809691 | 2.7128027681660898 | 2.9100346020761245 | 3.1141868512110724
RF power scan | 0.0095541 | 0.007896 | 0.0066348 | 0.0056533 | 0.0048746 | 0.0042463 | 0.0037321 | 0.0033059 | 0.0029488 | 0.0026466 | 0.0023885 | 0.0021665 | 0.001974 | 0.0018061 | 0.0016587 | 0.0015287 | 0.0014133 | 0.0013106 | 0.0012186 | 0.001136 | 0.0010616
At 1.7 gauss, = 0.0036/gauss
= 0.0029/W

## Slide 69: Change in Ambient Field
Chart: Field Gradient Change
| 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1 | 1.1000000000000001 | 1.2 | 1.3 | 1.4 | 1.5 | 1.6 | 1.7 | 1.8 | 1.9 | 2 | 2.1
epsilon | 0.99945 | 0.9989 | 0.99835 | 0.9978 | 0.99725 | 0.99669 | 0.99614 | 0.99559 | 0.99504 | 0.99449 | 0.99394 | 0.99339 | 0.99284 | 0.99229 | 0.99174 | 0.99118 | 0.99063 | 0.99008 | 0.98953 | 0.98898 | 0.98843
At BRF = 1.7 gauss, = 0.0055/(dH/dz)

## Slide 70: Bailey inside the Halbach array performing field mapping (before Christmas 2012)

## Slide 71
Trap door (6”x6” = 12x3 PMs)
Scan across the array surface along the short axis of the array:
0.8 T
Quality Assurance
Notes: We then put an IU undergraduate student in the trap to measure the magnetic field. She manually scan and measure the field at every 1 mm intervel.

## Slide 72: Characterizations of the Magnetic Trap
Planar Halbach with discrete magnetization components modeled by
Brem is the remanence of the PMs (1.35 T): NdFeB
Each PM is 1” (height) x 0.5” (width) x 2” (length)
Field falloff from
the array surface
k = 0.1228/mm   = 51.14 mm
d = 12.78 mm = 0.503 in
Gap between magnets = 0.003 in
Magnetic viewing film placed on the cross-section of the PM array.
Notes: Ripples due to the discrete element of the PM.
Exponential decay constant tells use the periodicity of the array.
The gap size is 3 mils, within the specification of mechanical design.

## Slide 73
Imperfections
1. P.L. Walstrom et al. Nucl. Instr. and Methods in Phys. Res. A 599 (2009) 82–92
y
x
By
Bz
|B|
Defects in Magnet Array
(~ 20 spots)
Field mapping (3D Hall probe)
Notes: Local dip in the magnetic field strength, that don’t quite recover to the required 0.8 T.

## Slide 74: Simulation on Defects
Comsol simulation
Chip on vertical M
Comsol:
Chip on horizontal M

## Slide 76
UCN trapping potential  50 neV
H=0.5 m in Earth gravity.
B=0.8 T (2 mm away from the array surface)

## Slide 77: Magnetic Field Simulations
Comsol Software (Finite Element Analysis): Geometry Creation, Mesh generation, Field solution, PMs modeled as ideal magnets (χm = 0); Guide Coils carry 300 Amps. Use IU supercomputer cluster (Mason), each node has 512 Gb of RAM.
Field In the vicinity of the Trap door (maximum mesh: 5 mm)

## Slide 78: UCN Spectrum (C. Morris)
Chart: Velocity (cm/sec)
v3dv distribution, due to absorption and
other losses in a thick D2 source.
Chart: Height (cm)
Raise the experiment by 1 m
SS guide: 190 neV

## Slide 79
V detector
E-dependent draining time
  E-dep. Absorption, slow oxidation of V foil: measure V draining time.
  E-dep. collision rate
  Uncertainties in deciding the “t_measure”.
  Change of draining time (phase space evolution)
  Height scan (UCN E spec.)
Small S/N, low gamma efficiency (due to non-uniform foil exposure, phase space evolution).
T-dep. Background
  Iodine thermal neutron activation
Gain drift
  B field (Hall probe monitoring)
  Calibration sources: LED pulser (beta scintillator)
  Monitor PHS for 1.4 MeV gamma (NaI)
Fill’n Dump
E-dependent draining time & detection efficiency
  Loss in the draining channel
  E-dep. draining time from the trap: monitored using MCS spectrum
  Uncertainties in deciding the “t_measure”.
Large S/N, low neutron background
  Thermal neutron efficiency & background
Gain drift
  long-term drift of PHS due to air contamination: monitor PHS

## Slide 80: Fermi potential vs thin-film oxide layer
Calculated without loss
in the film

## Slide 81
Loss in the thin film
V51
abs = 4.9 barns
V = -7.5 neV
Au197
abs = 98.65 barns
V = 116.54 neV
Ni
abs = 4.49 barns
V = 243 neV

## Slide 82: 51V neutron activation
: Emax= 2541.5 keV

## Slide 83: Iodine background
Iodine (I127 is the only stable isotope) decays. It has both beta decay (93.1%) and electron capture (6.90%) channels. The decay lifetime is 25min, comparable to our run cycle time.